## Slide 1
MICROPROCESSOR AND COMPUTER ARCHITECTURE LABORATORY
4TH Semester(UE19CS256)
Prof Deepti C
Computer Science and Engineering
Class 4 Week3
Saturday, January 30, 2021

## Slide 2
Microprocessor & Computer Architecture Laboratory
WEEK 3 | Write an ALP to add two 64 bit numbers loaded from memory and store the result in memory. Write an ALP to copy n numbers from Memory Location A to Memory Location B Write an ALP to find smallest number in an array of n 32 bit numbers a)Write an ALP to count the number of 1’s and 0’s in a given 32 bit number. b)Write an ALP to find the number of zeroes, positive and negative numbers in a given array 5. Write an ALP to check whether a given number is present in array using Linear Search(Without SWI 0x02), if found move +1 to R6 and key position to R7 else move -1 to R6 ( if number not found) 6. Write an ALP to generate Fibonacci Series and store them in an array

## Slide 3
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 1
WEEK 3 | Write an ALP to add two 64 bit numbers loaded from memory and store the result in memory.
 | a: .word 12213443, 56657887 b: .word 98764532, 45326789 | 
 | Upper 32 bits | Lower 32 bits
a: .word | 56657887 (036087DF) | 12213443 (00BA5CC3)
b: .word | 45326789 (02B3A1C5) | 98764532 (05E306F4)
c: .word | 101984676 (061429A4) | 110977975 (069D63B7)
Algorithm
Declare the first 64 bit number in the first two locations of array A in .data segment
Declare the second 64 bit number in the first two locations of array B in .data segment
Initialise initial sum =0 in Location C
Copy the lower word of the first number from location A to R4
Copy the lower word of the second number from location B to R5
Add the two lower words
Addition result is saved in R4
Store the lower word of the addition result in first location of array C
Copy the upper word of the first number from location A to R4
Copy the upper word of the second number from location B to R5
Add the two upper words
Addition result is saved in R6
Store the upper word of the addition result in second location of array C
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 4
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 2
WEEK 3 | Write an ALP to copy n numbers from Memory Location A to Memory Location B
.data a: .word 10, 20, 30, 40,50 b: .word 0, 0, 0, 0,0 | 
1st Iteration | a: .word 0A, 14, 1E, 28,32 b: .word 0A, 0, 0, 0,0
2nd Iteration | a: .word 0A, 14, 1E, 28,32 b: .word 0A, 14, 0, 0,0
3rd Iteration | a: .word 0A, 14, 1E, 28,32 b: .word 0A, 14, 1E, 0,0
4th Iteration | a: .word 0A, 14, 1E, 28,32 b: .word 0A, 14, 1E, 28,0
5th Iteration | a: .word 0A, 14, 1E, 28,32 b: .word 0A, 14, 1E, 28,32
Algorithm
Declare the first location A in .data segment
Declare the second location B in .data segment
Let R0 contain address of A
Let R1 contain address of B
Let R3 contain number of elements in the array.
Copy the first element of A into a register R4
Increment r0 to point to the next location of A
Copy the value in temporary register R4 to the first location of B
Increment r1 to point to the next location of B
Decrement the count of elements in the array A
Repeat steps 6 to 10 until R3 is not equal to zero
End program
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 5
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 3
WEEK 3 | Write an ALP to find smallest number in an array of n 32 bit numbers
a: .word 3,10,4,2, 5, 6 | 
1st Iteration | R2=3,R3=10 (R3>R2)
2nd Iteration | R2=3, R3=4 (R3>R2)
3rd Iteration | R2=3, R3=2 (R3<R2)
4th Iteration | R2=2, R3=5 (R3>R2)
5th Iteration | R2=2, R3=6 (R3>R2)
Smallest number is present in R2 | 
Algorithm
Declare the array A in .data segment
Let R0 contain address of A
Let R1 contain number of elements in the array.
Copy the first element of A into R2
Increment r0 to point to the next location of A
Compare the first element with zero
If zero,end the program
Decrement the number of elements in R1 by 1
Copy the next element of A into R3
Increment r0 to point to the next location of A
If the 2nd element in r3 is lesser than the first element in r2,copy the smaller value in r3 to r2
Repeat steps 6 to 11 ,Continue till all elements have been compared.End program
If r3 is greater than r2, Repeat steps 6 to 11 ,Continue till all elements have been compared.
End program
One Screenshot -Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 6
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 4a
WEEK 3 | Write an ALP to count the number of 1’s and 0’s in a given 32 bit number.
r0, =0b11110000101001011111000010100100 |  | 
r1 | 32 | 
r2 | After execution | 15 (=0F in hex)
r3 | After execution | 17 (=11 in hex)
Algorithm
1.Let R0=the number in binary
2.Let R1 contain the constant 32
3. Let R2 contain the count for number of ones,initially zero
4.Let R3 contain the contain the count for number of zeroes,initially zero
5.Shift the contents of R0 to the right through carry one time
4.If carry=1 after shift ,increment the ones count in R2
5. If carry=0 after shift ,increment the zeroes count in R3
6.Decrement the count for number of bits in R1
7.Compare the value in R1 with zero
8.Repeat steps 5 to 7 for all 32 bits
9.End program.
One Screenshot-Choose your own value

## Slide 7
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 4b
WEEK 3 | b)Write an ALP to find the number of zeroes, positive and negative numbers in a given array
a:.word 20,30,0,40,50,0,-2,-4,-9 |  | 
R3 | 3 | 
R4 | 2 | 
R5 | 4 | 
Algorithm
Declare the array A in .data segment
Let R0 contain address of A
Let R3 contain the count for number of elements in array
Let R5 contain the count for number of positive numbers,initially zero
Let R4 contain the count for number of zeroes,initially zero
Let R3 contain the count for number of negative numbers,initially zero
Copy the first element of array to R2
Check if element equal to zero,increment count in R4.Continue check for remaining array elements
If element is greater than zero,increment count in R5
Continue check for remaining array elements
10. If element is lesser than zero,increment count in R3
Continue check for remaining array elements
11.End program
One Screenshot-Choose your own value
for array elements

## Slide 8
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 5
WEEK 3 | Write an ALP to check whether a given number is present in array using Linear Search(Without display messages- SWI 0x02), if found move its position to R7 else move -1 to R6 ( if number not found)
 |  | HEX value
A:.WORD 10,20,30,40,50 |  | 
R2 | KEY =30 | 1E
R3 | COUNT =5 | 
R0 | Address of A | 00001034
R3 | After Execution =3 | Position of key element =3
Algorithm
Declare the array in .data segment
Initialise key element in register R2
Initialise count= number of values in the array in R3
Let R0=Address of A
Get the first element into register R1
Increment R0 to get next element of array A
Compare value in R1 with key element
If there is a match ,key is FOUND,go to Label1
If no match ,decrement the count value in R3
Repeat steps 5 to 9 till R3=0
Save -1 in R6 if key not found and terminate the program
At Label1,subtract (n+1) from R3.Save this value in R7 to get the position
End program
Two Screenshots -Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.Show key found and key not found.

## Slide 9
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 6
WEEK 3 | Write an ALP to generate Fibonacci Series and store them in an array
R0 | Fibonacci Count | 6
R1 | Address of A | 
R2 | Initially 0 | 
R3 | Initially 1 | 
R4 | 1st Iteration | 0+1=1
R4 | 2nd Iteration | 1+1=2
R4 | 3rd Iteration | 2+1=3
R4 | 4th Iteration | 3+2=5
R4 | 5th Iteration | 5+3=8
R4 | 6th Iteration | 8+5=13 =0D
Algorithm
Initialise array A in .data segment
Let R0 contain the count of Fibonacci Numbers
Let R1 contain address of array A
Let R2 contain Initial first number=0
Let R3 contain Initial second number=1
Save the number from R2 in the first memory location of A
Increment R1 to get the next location of array A
Save the second number from R3 in the second memory location of A
Increment R1 to get the next location of array A
Add both numbers in R2 and R3.Save addition result in R4
Copy the addition result in R4 into next location of array A
Add the previous two addition results to get the next fibonacci number
Decrement count in R0
Repeat steps 9 to 12 until R0 is not equal to zero
End Program
.
(
One Screenshot including Code,Register,Memory Window showing all the Fibonacci Values.Choose your own Count.

## Slide 10
deeptic@pes.edu
THANK YOU
Deepti C
Department of Computer Science and Engineering