## Slide 1
MICROPROCESSOR AND COMPUTER ARCHITECTURE LABORATORY
4TH Semester(UE19CS256)
Prof Deepti C
Computer Science and Engineering
Class 5 Week4
Monday, February 8, 2021

## Slide 2
Microprocessor & Computer Architecture Laboratory
WEEK 4 | Write an ALP to implement C[i]=a[i]+b[i] Write an ALP to implement c[k] = a[i] * b[j] a)Write an ALP to perform Convolution using MUL instruction (Addition of multiplication of respective numbers of loc A and loc B) b) Write an ALP to perform Convolution using MLA instruction (Addition of multiplication of respective numbers of loc A and loc B). 4.Write an ALP to read from a 2D array such that B=a[i] [j] 5. Write an ALP to implement C[i][j]=a[i][j]+b[i][j] 6. Write an ALP to implement Sum[i]+=a[i][j]

## Slide 3
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 1
WEEK 4 | Write an ALP to implement c[i]=a[i]+b[i]
 | a: .word 10, 20, 30, 40, 50 b: .word 10, 20, 30, 40, 50 c: .word 0,0,0,0,0 | 
After Execution The content of array C is |  | 
 | 20 | 00000014
 | 40 | 00000028
 | 60 | 0000003C
 | 80 | 00000050
 | 100 | 00000064
Algorithm
Declare the arrays A,B,C in .data segment
Let R0 contain address of A
Let R1 contain address of B
Let R2 contain address of C
Let R6 contain number of elements in the array.
Copy the element of A into a register R3
Increment r0 to point to the next location of A
Copy the element of B into a register R4
Increment r1 to point to the next location of B
Add the elements of A and B.Save the addition result in R5.
Store the addition result into the memory location of array C
Increment r2 to point to the next location of C
Decrement the count of elements(R6) in the array
Repeat steps 6 to 13 until R6 is not equal to zero
End program
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 4
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 2
WEEK 4 | Write an ALP to implement c[i] = a[i] * b[i]
 | a: .word 10, 20, 30, 40, 50 b: .word 10, 20, 30, 40, 50 c: .word 0,0,0,0,0 | 
After Execution The content of array C is |  | 
 | 100 | 00000064
 | 400 | 00000190
 | 900 | 00000384
 | 1600 | 00000640
 | 2500 | 000009C4
Algorithm
Declare the arrays A,B,C in .data segment
Let R0 contain address of A
Let R1 contain address of B
Let R2 contain address of C
Let R6 contain count=number of elements in the array.
Check if number of elements is zero,if zero end program
Decrement count by 1
Copy the element of A into a register R3
Increment r0 to point to the next location of A
Copy the element of B into a register R4
Increment r1 to point to the next location of B
Multiply the elements of A and B.
Save the result in R5.
Store the result into the memory location of array C
Increment r2 to point to the next location of C
Repeat steps 6 to 15 until R6 is not equal to zero
End program
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 5
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 3a,3b
WEEK 4 | a)Write an ALP to perform Convolution using MUL instruction (Addition of multiplication of respective numbers of loc A and loc B) such that the value ∑(a[i]*b[i]) is computed. Write an ALP to perform Convolution using MLA instruction (Addition of multiplication of respective numbers of loc A and loc B).
 | a: .word 10, 20, 30, 40, 50 b: .word 10, 20, 30, 40, 50
R5 | (10*10)+(20*20)+(30*30) +(40*40)+(50*50) =3000=00000bb8
Algorithm
Declare the arrays A,B in .data segment
Let R0 contain address of A
Let R1 contain address of B
Let R2 contain number of elements in the array.
Initialise sum=0 in r5.
Copy the element of A into a register R3
Increment r0 to point to the next location of A
Copy the element of B into a register R4
Increment r1 to point to the next location of B
Multiply the elements of A and B.
Save the multiplication result in R6.
Calculate sum=sum+multiplication result.
Decrement the count of elements(R2)
Repeat steps 6 to 13 till R2 is not equal to zero
End program
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.

## Slide 6
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 4
WEEK 4 | Write an ALP to read from a 2D array such that B=a[i] [j]
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.
Before execution | a:.word 1,2,3,4,5,6,7,8,9 | b: .word 0
After Execution | 00000001 | 00000001
 | 00000002 | 00000002
 | 00000003 | 00000003
 | 00000004 | 00000004
 | 00000005 | 00000005
 | 00000006 | 00000006
 | 00000007 | 00000007
 | 00000008 | 00000008
 | 00000009 | 00000009

## Slide 7
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 5
WEEK 4 | Write an ALP to implement C[i][j]=a[i][j]+b[i][j]
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.
Before execution | a:.word 1,2,3,4,5,6,7,8,9 | b:.word 1,2,3,4,5,6,7,8,9 | c:.word 0
After Execution | 00000001 | 00000001 | 00000002
 | 00000002 | 00000002 | 00000004
 | 00000003 | 00000003 | 00000006
 | 00000004 | 00000004 | 00000008
 | 00000005 | 00000005 | 0000000A
 | 00000006 | 00000006 | 0000000C
 | 00000007 | 00000007 | 0000000E
 | 00000008 | 00000008 | 00000010
 | 00000009 | 00000009 | 00000012

## Slide 8
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 6
WEEK 4 | Write an ALP to implement Sum[i]+=a[i][j]
One Screenshot-Choose your own value for array elements.Show the Memory Window,Code window and Register Window in the screenshot.
Before execution | a:.word 1,2,3,4,5,6,7,8,9 |  | 
After Execution | Addition result | 45 | 2D

## Slide 9
deeptic@pes.edu
THANK YOU
Deepti C
Department of Computer Science and Engineering